CCNA Discovery

Working at a Small-to-Medium Business or ISP

Lab 5.3.9 Password Recovery Procedures

| Device | Host Name | Interface | IP Address | Subnet Mask | Enable secret password | Enable/VTY/ and Console passwords |
| --- | --- | --- | --- | --- | --- | --- |
| R1 | GAD | Fast Ethernet 0/0 | 10.10.0.1 | 255.255.255.248 | class | cisco |

Objective

Gain access to a router with an unknown privileged mode (enable) password.

Background / Preparation

This lab demonstrates gaining access to a router with an unknown privileged mode (enable) password. One point to be made here is that anyone with this procedure and access to a console port on a router can change the password and take control of the router. That is why it is of critical importance that routers also have physical security to prevent unauthorized access.

Setup a network as displayed in the figure. Any router that meets the interface requirements may be used. Possible routers include 800, 1600, 1700, 2500, 2600 routers, or a combination. Refer to the chart at the end of the lab to correctly identify the interface identifiers to be used based on the equipment in the lab. The configuration output used in this lab is produced from 1721 series routers. Any other router used may produce slightly different output.

Required Resources

The following resources are required:

Router

A Windows-based PC with a terminal emulation program

RJ-45-to-DB-9 connector console cable

Note: Configure the hostname and passwords on the router. Have an instructor, lab assistant, or other student change the enable secret password. Perform copy running-config startup-config and reload the router.

Step 1: Attempt login to the router.

- Make the necessary console connections and establish a HyperTerminal session with the router. Attempt to logon to the router using the enable password cisco. The output should look like the following:

Router>enable

Password:

Password:

Password:

% Bad secrets

Router>

Step 2: Document the current config-register setting

- At the user EXEC prompt type show version.

- Record the value displayed for configuration register ___________. For example 0x2102.

Step 3: Enter the ROM Monitor mode

- Turn the router off, wait a few seconds and turn it back on. When the router starts displaying “System Bootstrap, Version …” on the HyperTerminal screen, press the Ctrl key and the Break key together. The router will boot in ROM monitor mode. Depending on the router hardware, one of several prompts such as: "rommon 1 >" or simply “>” may show.

Step 4: Examine the ROM Monitor mode help

- Type ? at the prompt. The output should be similar to this:

rommon 1 >?

| alias | set and display aliases command |
| --- | --- |
| boot | boot up an external process |
| break | set/show/clear the breakpoint |
| confreg | configuration register utility |
| context | display the context of a loaded image |
| dev | list the device table |
| dir | list files in file system |
| dis | display instruction stream |
| help | monitor builtin command help |
| history | monitor command history |
| meminfo | main memory information |
| repeat | repeat a monitor command |
| reset | system reset |
| set | display the monitor variables |
| sysret | print out info from last system return |
| tftpdnld | tftp image download |
| xmodem | x/ymodem image download |

Step 5: Verify the configuration of the switch.

- From the ROM Monitor mode, type confreg 0x2142 to change the config-register.

rommon 2 >confreg 0x2142

Step 6: Restart Router

- From the ROM Monitor mode, type reset or power cycle the router.

rommon 2 >reset

- Due to the new configuration register setting, the router will not load the configuration file. The system prompts:

"Would you like to enter the initial configuration dialog? [yes]:"

Enter no and press Enter.

Step 7: Determine which MAC addresses that the switch has learned.

- Now at the user mode prompt Router>, type enable and press Enter to go to the privileged mode without a password.

- Use the command copy startup-config running-config to restore the existing configuration. Since the user is already in privileged EXEC no password is needed.

- Type configure terminal to enter the global configuration mode.

- In the global configuration mode type enable secret class to change the secret password.

- While still in the global configuration mode, type config-register xxxxxxx. xxxxxxx is the original configuration register value recorded in Step 2. Press Enter.

- Use the Ctrl z combination to return to the privileged EXEC mode.

- Use the copy running-config startup-config command to save the new configuration.

- Before restarting the router, verify the new configuration setting. From the privileged EXEC prompt, enter the show version command and press Enter.

- Verify that the last line of the output reads:

Configuration register is 0x2142 (will be 0x2102 at next reload).

j. Use the reload command to restart the router.

Step 8: Verify new password and configuration

- When the router reloads the enable password should be class.

Upon completion of the previous steps, logoff by typing exit. Turn the router off.

Erasing and reloading the router

- Enter privileged EXEC mode by typing enable.

Router>enable

In privileged EXEC mode, enter the erase startup-config command.

Router#erase startup-config

The responding line prompt is:

Erasing the nvram filesystem will remove all files! Continue?

[confirm]

- Press Enter to confirm.

The response is:

Erase of nvram: complete

- In privileged EXEC mode, enter the reload command.

Router(config)#reload

The responding line prompt is:

System configuration has been modified. Save? [yes/no]:

- Type n, and then press Enter.

The responding line prompt is:

Proceed with reload? [confirm]

- Press Enter to confirm.

In the first line of the response is:

Reload requested by console.

After the router has reloaded the line prompt is:

Would you like to enter the initial configuration dialog? [yes/no]:

- Type n, and then press Enter.

The responding line prompt is:

Press RETURN to get started!

- Press Enter.

The router is ready for the assigned lab to be performed.

Router Interface Summary Table

| Router Interface Summary |
| --- |
| Router Model | Ethernet Interface #1 | Ethernet Interface #2 | Serial Interface #1 | Serial Interface #2 |
| 800 (806) | Ethernet 0 (E0) | Ethernet 1 (E1) |  |  |
| 1600 | Ethernet 0 (E0) | Ethernet 1 (E1) | Serial 0 (S0) | Serial 1 (S1) |
| 1700 | Fast Ethernet 0 (FA0) | Fast Ethernet 1 (FA1) | Serial 0 (S0) | Serial 1 (S1) |
| 1800 | Fast Ethernet 0/0 (FA0/0) | Fast Ethernet 0/1 (FA0/1) | Serial 0/0/0 (S0/0/0) | Serial 0/0/1 (S0/0/1) |
| 2500 | Ethernet 0 (E0) | Ethernet 1 (E1) | Serial 0 (S0) | Serial 1 (S1) |
| 2600 | Fast Ethernet 0/0 (FA0/0) | Fast Ethernet 0/1 (FA0/1) | Serial 0/0 (S0/0) | Serial 0/1 (S0/1) |
| Note: To find out exactly how the router is configured, look at the interfaces. The interface identifies the type of router and how many interfaces the router has. There is no way to effectively list all combinations of configurations for each router class. What is provided are the identifiers for the possible combinations of interfaces in the device. This interface chart does not include any other type of interface, even though a specific router may contain one. An example of this might be an ISDN BRI interface. The information in parenthesis is the legal abbreviation that can be used in Cisco IOS commands to represent the interface. |